OVERVIEW:

General Permit allows for intermediate stockpiles at a mining site not qualifying as inert under A.R.S. § 49-201(19).

SUPPLEMENTAL APPLICATION REQUIREMENTS:

1. Notice of Intent to Discharge (NOI) Form for a Type 2 General Permit

I have completed and attached this NOI Supplement form to the Type 2 General Permit NOI.

2. Provide a narrative description of the stockpile addressed under this permit. Specify the expected dates of operation, and the rate and volume of the material to be stockpiled. Include the nature of material, proposed location, and area of the footprint, maximum height and overall slope angle of the intermediate stockpile. (Attach additional pages as necessary.)

2. Provide engineering drawings and specifications, a design report and operation plan that demonstrates:

The stockpile is designed, constructed and operated not to impound water. Include any run on controls, facility design features such as drains, or both.

Inspections will be performed at least quarterly to ensure the design and performance, with any necessary repairs performed as soon as possible.

All storm water runoff contacting the pile will be directed to a mine pit or other facility permitted under the aquifer protection program.

All engineered features designed to aid compliance with this permit will be adequately maintained.

That no hazardous substances will be added to the stockpile